SHIP’S MAIN PARTICULARS

NAME OF SHIP : M.V.“BEI JIANG”（“达通北江”轮）

## TYPE:  GLESS / NO CELL-GUIDE GENERAL CARGO SHIP

#### ICE CLASS: B

BUILT : 2005/ P.R.CHINA

CLASSIFICATION :CCS

DEADWEIGHT / SUMMER DRAFT: 7633MT /6.50M

GROSS/NET TONNAGE : 5,250/2,976

CALL SIGN/IMO NO.: V3UK7 / 9364710

MOBILE: 13904159701

E-MAIL: ddmscbeijiang@126.com

FLAG / PORT OF REGISTRY : BELIZE / BELIZE CITY

L.O.A. /BREADTH/DEPTH : 110.00 M /19.70 M/8.50M

CONTAINER STOWAGE: TOTAL 562TEUS

IN HOLD: 181TEUS

ON DECK: 381TEUS(170FEUS+41TEUS)

## STABILITY ABT 357TEU ON 14MT HOMOGENEOUS

STRENGTH OF TANKTOP/DECK/HATCHES:

### HOLD: 54/90MTS PER 20'/40' STACK

HATCHES OR MAIN DECK: 45/60MTS PER 20'/40' STACK

REEFER SOCKETS  : 30 PCS ON DECK(380V/440V)

DANGEROUS CARGO: 01BAY-19BAY ON DECK

BUNKER CAPACITY: FO 289.996CBM     MGO59.909CBM

FRESH WATER:    159.45 CBM

BALLAST WATER:  3953.70 CBM

HOLDS /HATCHS: 3HOLDS/ 3HATCHES (11PCS OF PONTOON TYPE HATCH COVERS / 16-24MT/PC)

(2TIER OF 8’6” PLUS 1TIER OF 9’6” COULD BE LOADED IN CARGO HOLDS)

MAIN ENGINE: Zichai-LB8250ZLC-7*2  MCR:1470 KW*2

AUXILLARY ENGINE: WD61568CD*3  170KW*3

GENERATOR : 150GFCB-HW6*3  150KW*3

SPEED/CONSUMPTION: 11.50 KNOTS ON 10.50 MT 180CST & ABT 0.60MT MGO

A/E CONSUMPTION IN PORT: 0.50MT / MGO