SHIP’S MAIN PARTICULARS

NAME OF SHIP : M.V.“EASLINE NINGBO” （“大通宁波”轮）

TYPE:  2 X 40MT CRANES / CELLULAR CONTAINER SHIP

BUILT : SEPT.2003, CHINA

CLASSIFICATION : KR

DEADWEIGHT /SUMMER DRAFT:   20,169MT / 10.78M

GROSS/NET TONNAGE : 16,145 / 8,857

CALL SIGN / IMO NO ：H3ZP / 9256418

INMARSAT TLX (SATCOM C): C1:437409112 / C2:437409113

SSAS:437409114

MASTER’S MP NUMBER IN CHINA: 13952007470

MASTER’S E-MAIL ADDRESS IN CHINA PORTS: easlineningbo@163.com

EMAIL：revert

TEL: revert

FAX: revert

FLAG / PORT OF REGISTRY : PANAMA / PANAMA

L.O.A./L.B.P./BREADTH/DEPTH : 172.20M/162.81M/25.10M/14.20M

CARGO CAPACITY : IN HOLD 605TEU / 288FEU + 29TEU

ON DECK 976TEU / 488FEU

TOTAL 1,581TEU / 776FEU + 29TEU

## STABILITY 1,062TEU ON 14MT HOMOGENEOUS

STRENGTH ON HATCHCOVERS/DECK: 70MT PER 20’ STACK

90MT PER 40’ STACK

STRENGTH IN HOLDS: 120MT PER 20’STACK N 150MT PER 40’ STACK

REEFER PLUG :  288 REEFER PLUG Whereof 204 on deck and 84 under deck in hold no.4 +5 each 42 reef, 440volt, 60cycles, 3phases for teus/feus

TANKS CAPACITY : F.O.(380CST) ABT 1,220M3 / M.D.O. ABT 227M3

HOLDS/ HATCHES: 6 / 8

HATCHES TYPE: two longitudinal separated pontoon sections each hatch all pontoons can be operated non-sequential.

MAIN ENGINE: man/b+w 6 s 60 mcc

AUXILIARIES: 3 x 1260 kw

BOWTHRUSTOR: 1SET

SPEED / CONSUMPTION OF M/E: 20.00KNOTS/ 55.0MT MFO-380CST

CONSUMPTION OF A/E IN PORT& AT SEA : 3.00MT MFO-380CST