SHIP’S MAIN PARTICULARS

NAME OF SHIP : M.V.“LILA BHUM” （“达通三亚”轮）

TYPE:  2X40MT CRANES / CELLULAR CONTAINER SHIP

BUILT : 1997 / JAPAN

CLASSIFICATION : NKK

DEADWEIGHT /SUMMER DRAUGHT:   10,908MT / 8.00M

LIGHT WEIGHT : 4,501MT

GROSS/NET TONNAGE :8,443/4,228

IMO NO / OFFICIAL NO：9143465 / 387468

E-Mail: lila.bhum@rclship.com

Telephone: 870-773170699

INM-C: 456424110

MMSI: 564241000

FLAG / PORT OF REGISTRY : SINGAPORE / SINGAPORE

L.O.A./L.B.P./BEAM/DEPTH : 135.90M/126.18M/22.00M/11.00M

CARGO CAPACITY : IN HOLD 290TEU

ON DECK 575TEU

TOTAL 865TEU

## STABILITY 581TEU ON 14MT HOMOGENEOUS

STRENGTH ON HATCHCOVERS/DECK: 60MT PER 20’ STACK

90MT PER 40’ STACK

STRENGTH IN HOLDS: 96MT PER 20’STACK N 120MT PER 40’ STACK

REEFER CONTAINER :  132 SOCKETS on Deck

TANKS CAPACITY : MFO 908M3 / MDO 50M3

WATER BALLAST 3,349M3 / F.W. 187M3

HATCHCOVER TYPE: PONTOON TYPE

HOLDS/ HATCHES: 5 / 13

MAIN ENGINE: AKASAKA-MITSUBISHI 6UEC 45LA / 5,300KW

AUXILIARY ENGINES: YANMAR, 6M 220 AL-UN, 3X680KW

BOWTHRUSTOR: 1SET / 675KW

SPEED / CONSUMPTION OF M/E: 16.0KNOTS / 24.00MT MFO-380CST

15.5KNOTS / 21.00MT MFO-380CST

15.0KNOTS / 19.50MT MFO-380CST

14.5KNOTS / 18.00MT MFO-380CST

A/E CONSUMPTION AT SEA/IN PORT: 2.20MT MFO-380CST